## Slide 1: The dsPIC33EP256GM710
A Breadboarding adventure!

## Slide 2
Available on Digikey!

## Slide 3
100 pin TQFP
Package
256 KB RAM
3.3 V Supply
Nice, but how do you breadboard this?

## Slide 4
How to breadboard?
Proto-advantage makes a carrier and will solder the IC for you!

## Slide 5
A couple days later, the part shows up!
Nice!

## Slide 6
VDD (+3.3V)
dsPIC pins 2, 16, 37,46,62,86 to +3.3V bus
VSS (GND)
dsPIC pins 15,36,45,65,75 to GND bus
AVDD dsPIC pin 30 (to +3.3V bus)
AVSS dsPIC pin 31 (to GND bus)
VCAP dsPIC 85 to 10 uF cap other end to GND bus
PICKIT3 CONNECTIONS
1 – MCLR dsPIC PIN 13 (see next Figure)
2 – VDD (+3.3 bus)
3 – VSS (GND bus)
4 – dsPIC PIN PGED 27
5 – dsPIC PGEC 26
Add decoupling caps (0.1 uF) across VCC, VSS
Breadboard connections

## Slide 7
MCLR and PICKIT PIN 1 Connections
2 resistors: 10k, 460 Ohms;
1 capacitor: 0.1 uF

## Slide 8
LED Connection PORT E PIN 1

## Slide 9
3.3V Power from ADAFruit USB Breakout board and LD1117V33C Linear Regulator

## Slide 10
NOW THE CODE IN MPLABX!